Energy consumption in South Asia

1.1 Energy consumption in India

Energy consumption, economic growth, and population are interlinked. In case of India, the country’s total primary energy supply (TPES) over the decades has kept pace with the rising income and population. It has grown from a modest figure of 147.5 million tonnes of oil equivalent (MTOE) in 1970 to approximately 437.69 MTOE, thereby growing at an average annual growth rate of 5.19% (TEDDY, 2002/03). The country has seen an expansion in the total energy use for the past five decades, with a shift from non-commercial to commercial energy sources. The share of commercial energy has risen over the years from nearly 41.02% to 68.23% of TPES in spite of dominance of non-commercial forms of energy in rural India.

Coal is the most abundant among all the commercial energy sources, and its production has increased at an average annual growth rate of 5.11%, during 1970-2001. Its share in the total commercial energy supply has, however, declined from a level of 60.47% (36.48 MTOE) in 1970-71 to 44.8% (133.89 MTOE) in 2001/02 primarily due to increase in the share of inferior grade coal in the overall coal production (TEDDY, 2002/03). Indigenous coal has always been the most stable and least expensive option for meeting bulk of the India’s energy needs, especially for power generation.

The petroleum and natural gas sector has registered a robust growth in domestic production and supply over the ten years, though the country continues to depend on crude oil imports. Domestic oil production has registered a growth of nearly 5.33% per annum during the 1970-2000 period, though India’s net import of crude oil has increased from 12.43 million tonnes to 75 million tonnes in the same period (MoPNG 2002). This is because the consumption of petroleum products has increased in all sectors, especially in the transport and industry sector.

The bulk of the energy needs of the domestic sector are met through non-commercial fuels such as fuelwood and dung. The rural household sector, which is the largest energy- consuming sector accounting for 75% of the total energy consumed by the domestic sector, depends largely on traditional fuels (TEDDY, 2002/03).  Rural household are dependent on biomass fuels such as fuelwood, cow dung and agricultural residue.

1.1.1 Sectoral energy consumption

Consumption of solid fuels and petroleum products in India during the period 1990-91 to 1999-00 is shown in the Tables 1.1 and 1.2, respectively and the same is depicted graphically in Figures 1.1 and 1.2, respectively.

Table 1.1  Solid fuel consumption (in thousand tonnes) in  India during the period 1990- 91 to

1999-00

|  | Coal | Lignite | Fuelwood | Agricultural residue | Dung cake |
| --- | --- | --- | --- | --- | --- |
| 1990-91 | 190382 | 14110 | 146748 | 88185 | 106824 |
| 1991-92 | 209521 | 15970 | 148993 | 88251 | 106421 |
| 1992-93 | 222706 | 16620 | 151395 | 88317 | 106024 |
| 1993-94 | 252592 | 18100 | 153967 | 88383 | 105632 |
| 1994-95 | 241382 | 19340 | 156714 | 88449 | 105244 |
| 1995-96 | 261356 | 22140 | 157913 | 88515 | 104862 |
| 1996-97 | 275657 | 22540 | 160076 | 88582 | 104484 |
| 1997-98 | 284571 | 23050 | 162400 | 88648 | 104111 |
| 1998-99 | 274291 | 23170 | 164884 | 88715 | 103743 |
| 1999-00 | 289300 | 22120 | 167525 | 88781 | 103379 |

Table 1.2  Petro-product consumption (in thousand tonnes) in India during the period       1990- 91 to 1999-00

|  | SKO | LPG | MS | HSD | LDO | FO | HSS/LSHS |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 1990-91 | 8419 | 2414 | 3543 | 21202 | 1487 | 4374 | 4427 |
| 1991-92 | 8391 | 2649 | 3570 | 21749 | 1436 | 4868 | 4121 |
| 1992-93 | 8579 | 2872 | 3613 | 24520 | 1378 | 5171 | 3965 |
| 1993-94 | 8998 | 3111 | 3832 | 25868 | 1338 | 4922 | 4124 |
| 1994-95 | 8959 | 3431 | 4142 | 28371 | 1347 | 5775 | 4052 |
| 1995-96 | 9312 | 3812 | 4684 | 32081 | 1290 | 6268 | 4189 |
| 1996-97 | 9641 | 4179 | 4945 | 35110 | 1197 | 6178 | 4354 |
| 1997-98 | 9870 | 4579 | 5179 | 36004 | 1203 | 6392 | 4388 |
| 1998-99 | 10552 | 5053 | 5508 | 36813 | 1242 | 6198 | 4506 |
| 1999-00 | 10722 | 6026 | 5905 | 39162 | 1488 | 6607 | 4701 |

Note: 	SKO - Superior kerosene oil

LPG - Liquefied petroleum gas

MS - Motor spirit

HSD - High speed diesel oil

LDO - Low sulphur diesel oil

FO - Fuel oil

HSS/ LSHS - Hot heavy stock/ Low sulphur heavy stock

Figure 1.1 Consumption of solid fuels in India during the period 1990-91 to 1999-00

Figure 1.2  Consumption of Petro-products in India during the period 1990-91 to 1999-00

Coal consumption

Figure 1.3  Coal consumption in power and industrial sectors in India during the period 1990-91 to 1999-00

Coal has taken center-stage in India’s energy scenario. Figure 1.3 shows consumption of coal in power and industrial sectors for the years 1990-91, 1994-95 and 1999-00. Its dominance continues unabated primarily because power generation favours this fuel, given its indigenous availability. About 70% of coal produced is consumed by the power sector. In addition, other industries like steel, cement, fertilizer, chemicals and thousands of medium and small-scale industries also depend on coal for their process and energy requirements. In the transport sector, though direct consumption of coal is reducing due to phasing out of steam locomotives, the energy requirement for electric traction is still dependent on coal (MoC, 2003).

Oil and gas

Despite the discovery of new sources of unconventional energy, petroleum remains the primary energy source in India. The consumption of petroleum is increasing at a very steep rate from 3.5 MMT in 1950-51 to 74.7 MMT in 1995-96. This is expected to reach 130 MMT in 2001-2002 and 175 MMT in 2006-2007 (MoPNG, 2004). The consumption of petro-products in different sectors during the period 1990-91 to 1999-00 is shown in Annexure-I.

Power Sector

The Indian power sector, the backbone of nation’s development, has gradually evolved over the years. After independence, India’s installed generation capacity was mere 1.3 GW (gigawatt), while today it is more than 100 GW. Annual gross generation in utilities has grown at an average annual growth rate of approximately 7.7%, during 1975-2001. Over the years, thermal power has continued its dominance over the aggregate power generation, and its share has increased from 54% to nearly 81% during the same time period (TEDDY, 2002/03). Industry is the largest consumer of power and its consumption has grown at the rate of nearly 4.2 % per annum in the last quarter of the 20th century.

Primary fuel that is consumed in power sector in India is coal; power sector consumes approximately seventy percent of coal. Apart from coal the other fuels that are consumed in the power sector are lignite, diesel oil, furnace oil, heavy stock, naphtha and natural gas

Industry Sector

The industrial sector consumes about 50% (including feed stocks) of the total commercial energy produced in the country. The total industrial energy consumption, including non-energy uses, grew from 45.7 MTOE (million tonnes of oil equivalent) in 1984/85 to 113.1 MTOE in 1996/97. Of the commercial sources of energy, coal and lignite contribute about 57%, oil and natural gas 33% (TEDDY 2002/03).

The energy intensive industries are iron & steel, cement, fertilizer, chemical & allied industries. The fuels that are consumed in these industries are coal, diesel oil, furnace oil & heavy stock.

Agriculture

Increased cropping intensity and modern agriculture necessitated higher energy inputs for field operations as well as agro-processing. One of the major engineering inputs adopted has been irrigation pump. The number of electrical and diesel pump need has increased from 1.6 million in 1970 to 13.0 million in 2001/02 (TEDDY, 2002/03).

Animal power has been supplemented by tractors, power tillers, diesel engines, and electric motors to a considerable extent. The share of agriculture sector in the total commercial energy consumption in India has increased from 1.7% in 1953/54 to 9.0% in 1990/91. The share of commercial energy uses like electricity, diesel, fertilizer and tractor power in the total energy consumption by the agriculture sector has increased from meagre 11% in 1951 to more than 90% in 2001/02 (TEDDY 2002/03). The primary fuel consumed in this sector is diesel oil.

Transport Sector

The transport mix in India – Road, Rail, Shipping and Aviation consume products of petroleum, road being the major mode of transport. There has been a tremendous increase in not only the number of registered vehicles but also the road network. In 2000, the number of registered vehicles was over 48 million (MoRTH, 2002). The transport sector consumes motor spirit, diesel oil, furnace oil and aviation fuel (ATF).

Domestic Sector

In Indian households, energy is mainly used for cooking, heating water and space, lighting, and preparing cattle feed. Cooking and lighting are the two main functions that consume energy, while importance of the other functions varies by region.

In urban areas, households use mainly three sources, namely, firewood, kerosene, and LPG as primary sources of energy for cooking. LPG is found to be the main source with 44% of households using it as a primary source for cooking. About 22% of households use firewood and chips as primary source of energy for cooking. The per capita monthly consumption of firewood and chips in urban areas has increased from 6.09 kg in 1993/94 to 6.45 kg in 1999/2000 (NSSO, 1997 & 2001). This trend shows that urban poor households are still dependent on traditional fuels for their energy needs.

In rural areas, according to the latest NSSO survey (1999-2000), 86.1 % of the rural households use fuelwood and dung for cooking. The comparison of the last two NSSO rounds (1993-94 & 1999-00) reveals that there is a slight decrease in the consumption of biomass based fuels for cooking. However, the decrease is negligible compared to share of biomass based fuels. There is a slight penetration of LPG in rural areas with an increase of 3.5% in the number of households using LPG for cooking.

1.1.2 Data collection methodology

The consumption of fuels in different sectors such as power, industry, domestic and transport sectors at state level was collected for a time period of ten years, from 1990-91 to 1999-00.

Coal and lignite

The statewise consumption of coal in different industrial sectors was collected from sales & marketing report of Coal India Limited (CIL). Coal despatches to different sectors from Singareni Collieries Company Limited (SCCL) were also collected from Coal Directory of India, Ministry of Coal. The combined despatch of CIL & SCCL is approximately 91% of the total coal despatch. The rest of the despatch (approximately 9%) is either from smaller coal companies or imported coal. Only the combined despatch of CIL and SCCL was collected and used for emission estimation, as the information on other sources of despatch, such as despatch destiny & end use sector is not available. The following assumptions were also made:

- Singareni Collieries Company Limited (SCCL) despatches coal to most of the customers situated in Andhra Pradesh and to some extent in other parts of Southern India. The customers are broadly categorized as core sector (Linked Consumers), non-core sector (Unlinked Consumers) (http://scclmines.com/customer_service.asp, June-2004). Since the exact despatch destination details were not available, the entire despatch was allocated to Andhra Pradesh. 80% of SCCL coal is being fed to Power Houses and about 12% goes to Cement Sector (http://scclmines.com/customer_service.asp, June-2004). The rest goes to non-core sectors. Accordingly despatch was allocated to these sectors.

- It is also assumed that whatever coal is despatched from these companies is consumed.

Lignite is consumed mainly in Tamil Nadu and Gujarat. Lignite consumption from these states was collected from Coal Directory of India, Ministry of Coal. It was assumed that in Tamil Nadu lignite is consumed in power sector. In the case of Gujarat power sector consumption data was collected from CEA (Central Electricity Authority), the difference in total consumption and power sector was allocated to industries.

Petro-products

Indian petroleum and natural gas statistics gives information on state level consumption of different petroleum products. It also gives estimates on sector-wise end use at the national level.  The state level consumption of petro-products was extrapolated to different sectors based on national sectoral end use. The following assumptions/estimates were made;

- It is assumed that kerosene oil is consumed only in the domestic sector, and, motor spirit and aviation turbine fuel in the transport sector.

- There is no system of capturing sector-wise sale of HSD through retail outlets (Resellers). This consumption was therefore allocated to other transport (including agriculture retail trade), which is approximately 73% of total HSD consumption. However, directional figures are available based on all India study conducted by IMRB (Indian Market Research Bureau) in 1998. These figures were used by the Ministry of Petroleum and Natural Gas (MoPNG) to revise their national sectoral end use of HSD from the year 1997 –98. Due to this revision the sectoral consumption of road transport has increased from meagre 8% to almost 53% from 1997-98 onwards. The directional figures by IMRB were used to reallocate HSD consumption into different sectors for the entire study period (1990-91 to 1999-00).

- The percentage consumption of HSD, FO, LDO and LSHS/HSS in different industries – steel, cement, fertilizer and non-core at state level was estimated from Annual Survey of Industries (ASI) statistics. These ratios were used to apportion total state level industrial consumption of HSD, FO, LDO and LSHS/HSS (from MoPNG statistics) to different industries – steel, cement, fertilizer and non-core.

Fuelwood, dung cake and crop residue

National Sample Survey Organisation (NSSO) collects information on state level consumption of domestic fuels in India. The consumption of firewood & chips for the study period was estimated based on two NSSO surveys - Monthly per capita consumption of firewood & chips in urban & rural areas for the years 1993-94 & 1999-00. The compounded annual growth rate (CAGR) was calculated based on these two surveys and was extrapolated to other years of the study period. The annual consumption was estimated by multiplying population (based on population Census-1981&1991&2001 as received from Registrar General of India) with monthly per capita consumption.

The consumption of agricultural crop residue and dung cake estimate is based on an earlier study conducted by TERI (1999). Consumption estimates of agricultural residue and dung cake for the years 1990 & 2000 under business as usual scenario was taken as basis.

The compounded annual growth rate (CAGR) was estimated based on these two years data and was interpolated for other years of the study period. The aggregate consumption in the Himalayan region was apportioned to the respective states based on cattle population & cultivable land area, whereas for other regions the data was available at state level.

1.2 Energy consumption in other South Asian Countries

Fossil fuel consumption data in other South Asian countries - Bangladesh, Nepal, Pakistan and Sri Lanka was collected from Energy Statistics of Non-OECD Countries, IEA (International Energy Agency).  The IEA statistics for Bhutan is not available. The consumption of coal and petro products in different sectors such as power, transport, industries, agricultural and domestic sectors was collected for the study period 1990 to 1999.

Fuel wood consumption data for the years 1990 to 1994 was collected for all five countries, including Bhutan, from Regional Wood Energy Development Programme (RWEDP). Consumption for rest of the years was estimated based on the projected percentage growth rate under BAU scenario (Web: http://www.fao.org/docrep/w7519e).  The conversion factors as stated in Table 1.3 were used to convert consumption in m3 to kg.

Table 1.3  Conversion factors for fuelwood (m3 to kg)

| Bangladesh | 650.4747 |
| --- | --- |
| India | 650.7322 |
| Nepal | 650.0907 |
| Pakistan | 651.1333 |
| Sri Lanka | 668.7484 |

The fuel consumption in other South Asian countries (Sri Lanka, Pakistan, Nepal and Bangladesh) during the period 1990 to 1999 is shown in Annexure –II and also given in Tables 1.4 to 1.6.

Table 1.4  Fuel consumption (in thousand tonnes)  in Sri Lanka during the period 1990-1999

|  | 1990 | 1994 | 1999 |
| --- | --- | --- | --- |
| Hard coal | 8 | 1 | 1 |
| LPG | 34 | 64 | 168 |
| MS | 179 | 184 | 213 |
| Jet fuel | 57 | 146 | 241 |
| Kerosene | 167 | 208 | 244 |
| Diesel oil | 548 | 804 | 1634 |
| Fuel oil | 159 | 267 | 671 |
| Fuelwood | 5433 | 5730 | 6164 |

Table 1.5  Fuel consumption (in thousand tonnes) in Pakistan during the period 1990-1999

|  | 1990 | 1994 | 1999 |
| --- | --- | --- | --- |
| Hard coal | 4245 | 4628 | 4371 |
| Charcoal | 0 | 179 | 212 |
| Natural gas (tera joules) | 449692 | 526561 | 613434 |
| LPG | 127 | 122 | 235 |
| MS | 821 | 992 | 1171 |
| Jet fuel | 455 | 553 | 758 |
| Kerosene | 1133 | 608 | 500 |
| Diesel oil | 4277 | 5912 | 6851 |
| Fuelwood | 15719 | 17838 | 21314 |

Table 1.6  Fuel consumption (in thousand tonnes) in Nepal during the period 1990-1999

|  | 1990 | 1994 | 1999 |
| --- | --- | --- | --- |
| Hard coal | 82 | 115 | 351 |
| LPG | 4 | 13 | 39 |
| MS | 16 | 25 | 40 |
| Jet fuel | 15 | 26 | 42 |
| Kerosene | 77 | 130 | 261 |
| Diesel oil | 110 | 182 | 263 |
| Fuel oil | 6 | 26 | 26 |
| Fuelwood | 11551 | 12809 | 14571 |

Table 1.7  Fuel consumption (in thousand tonnes) in Bangladesh during the period 1990-1999

|  | 1990 | 1994 | 1999 |
| --- | --- | --- | --- |
| Hard coal | 563 | 59 | 92 |
| Natural gas (tera joules) | 163997 | 225417 | 300118 |
| LPG | 9 | 13 | 10 |
| MS | 98 | 153 | 272 |
| Jet fuel | 86 | 90 | 130 |
| Kerosene | 475 | 392 | 586 |
| Diesel oil | 833 | 963 | 1482 |
| Fuel oil | 197 | 232 | 336 |
| Naphtha | 0 | 73 | 73 |
| Fuelwood | 18285 | 19918 | 22083 |

# Text boxes

1