Black carbon emission inventory

2.1 Introduction

Black carbon (BC) emissions were estimated annually for a period of ten years from 1990-91 to 1999-00 using fuel consumption data and appropriate BC emission factors.

Black carbon emission factors for various fuels were collected through detailed literature survey. The emission factors vary according to the type of fuel, technology/device used and type of emission control technology. Table 2.1 shows the black carbon emission factors for different fuels reported in the literature.

Table 2.1  Comparison of emission factors for Black Carbon.  (g/kg)

| Category | Black carbon |
| --- | --- |
|  | Cooke et al. (1999) under developed | Cooke et al. (1999), semi-developed | Reddy & Venkataraman (1999) | Gadi et al. (2001) | Cachier et al. (1989) |
| Coal | 2.13 | 1.22 | 1 |  | 3 |
| Diesel | 10 | 10 | 0.7 |  | 5 |
| Gasoline | 0.15 | 0.15 | 6 x 10-5 |  | 0.1 |
| Kerosene | 0.03 | 0.03 | 0.3 |  | 0.3 |
| Wood |  |  | 0.28 | 0.16 - 2.5 | 2.5 |
| Dung |  |  | 0.325 | 2.7 - 9.03 | 2 |
| Agriculture residue |  |  | 0.446 | 0.2- 2.7 |  |

Large variation in the emission factor presented in Table 2.1 reveals the high degree of uncertainty associated with black carbon emission factor. Information on technology or emission control devices is limited. This also highlights the need for the estimation of suitable emission factors.

2.2 Black carbon emission estimates for India

In the present study, we adopted the black carbon emission factors reported by Reddy & Venkataraman (1999) for various fuels except in case of gasoline. For gasoline the emission factor (0.1 g/kg) reported by Cachier et al (1989) was used to estimate the black carbon emission.

In addition, open burning of crop waste is also one of the sources of black carbon emission. Attempts were made to estimate black carbon emission from open burning of crop residues in India by applying the following formula.

Q = Quantity of crop residue (on dry basis)

B = Fraction of crop residue burned in the field

F= Crop specific burn efficiency ratio

E = Emission factor

State wise agricultural production of 14 crops for the period of 1990- 2000 was compiled from Agricultural statistics published by the Government of India and Fertilizer statistics (GOI, 2001; FAI, 2001). The crop production data was multiplied with crop specific residue to crop ratio and corresponding dry matter fraction reported by Koopmans and Koppejan (1997). In absence of any study or data on the quantity of agricultural residue burned in the field, the assumption used by Reddy et. al. (2002a) i.e 25% of crop residue produced are burned in the field was used in the present calculation.

The estimated BC emissions for the period 1990-91 to 1999-00 are presented in Table 2.2. Detailed fuel wise and sector wise BC emission estimates for India for the period 1990-2000 are given in Annexures III and IV, respectively.

Table 2.2  Black carbon emission estimates for India (Gg/year)

|  | 1990-91 | 1991-92 | 1992-93 | 1993-94 | 1994-95 | 1995-96 | 1996-97 | 1997-98 | 1998-99 | 1999-00 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Fuel Oil | 3.1 | 3.4 | 3.6 | 3.4 | 4.0 | 4.4 | 4.3 | 4.5 | 4.3 | 4.6 |
| HSD | 14.9 | 15.2 | 17.2 | 18.1 | 19.9 | 22.5 | 24.6 | 25.2 | 25.8 | 27.4 |
| SKO | 2.5 | 2.5 | 2.6 | 2.7 | 2.7 | 2.8 | 2.9 | 3.0 | 3.2 | 3.2 |
| MS | 0.4 | 0.4 | 0.4 | 0.4 | 0.4 | 0.5 | 0.5 | 0.5 | 0.6 | 0.6 |
| LPG | 0.1 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.3 | 0.3 | 0.3 | 0.4 |
| Coal | 190.4 | 209.5 | 222.7 | 252.6 | 241.4 | 261.4 | 275.7 | 284.6 | 274.3 | 289.3 |
| HSS | 3.1 | 2.9 | 2.8 | 2.9 | 2.8 | 2.9 | 3.0 | 3.1 | 3.2 | 3.3 |
| LDO | 1.5 | 1.0 | 1.0 | 0.9 | 0.9 | 0.9 | 0.8 | 0.8 | 0.9 | 1.0 |
| Lignite | 14.1 | 16.0 | 16.6 | 18.1 | 19.3 | 22.1 | 22.5 | 23.0 | 23.2 | 22.1 |
| Biomass | 115.1 | 115.7 | 116.2 | 116.9 | 117.5 | 117.8 | 118.3 | 118.9 | 119.5 | 120.1 |
| Open agri residue | 44.9 | 47.6 | 49.2 | 50.0 | 53.2 | 51.1 | 57.0 | 53.9 | 56.4 | 58.5 |
| Total fossil fuels | 230.1 | 251.0 | 266.9 | 299.3 | 291.7 | 317.7 | 334.6 | 345.0 | 335.6 | 351.9 |
| Total biomass | 160.0 | 163.2 | 165.4 | 166.8 | 170.7 | 168.9 | 175.3 | 172.7 | 175.9 | 178.6 |
| Total BC Emission | 390.1 | 414.2 | 432.4 | 466.1 | 462.4 | 486.6 | 509.9 | 517.7 | 511.5 | 530.5 |

Total black carbon emissions from India are 390 Gg during 1990-91 and 531 Gg in 1999-2000. In comparison, emission estimates from fossil fuel combustion and biomass combustion for the year 1990-91 are 230.1 Gg and 160 Gg. Over the last decade the share of BC emission from fossil fuel combustion has increased from 33% in 1990-91 to 41% in 1999-00.

The emission estimates are comparable to the emissions reported by Reddy and Venkataraman (1999), that is total black carbon emission from India for the year 1990 was 440 Gg out of which 240 Gg from fossil fuel and 200 Gg from biomass. However, the present estimates are lower than 687.9 Gg from fossil fuel combustion for the year 1990 reported by Mitra et. al. (2002). This variation is primarily due to the choice of emission factors. Black carbon emissions from biomass are not included in the estimates made by Mitra et. al. (2002). (Emission factors for under developed countries reported by Cooke et. al. (ref. Table 2.1) were used by Mitra et. al.2002)

Figure 2.1  Percentage share of BC emission from various sectors for the year 1999-2000.

Figure 2.1 reveals that power sector is one of the major contributors for the total BC emission in India, which is followed by domestic and industry.

2.3 Black carbon emission estimates for other South Asian

countries

#### Black Carbon emissions from other countries in South Asia were estimated in the similar way using the respective fuel consumption data. The estimate doesn’t include the emission from open biomass burning. The BC emissions for South Asian countries are presented in Table 2.3

Table 2.3  Total Black Carbon emission (in Gg) from other countries in South Asia

| Year | Bangladesh | Pakistan | Nepal | Srilanka |
| --- | --- | --- | --- | --- |
| 1990 | 7.8 | 8.3 | 3.4 | 2.0 |
| 1991 | 7.1 | 8.5 | 3.6 | 2.0 |
| 1992 | 7.3 | 9.1 | 3.7 | 2.2 |
| 1993 | 7.3 | 9.8 | 3.8 | 2.2 |
| 1994 | 7.5 | 10.6 | 3.9 | 2.3 |
| 1995 | 9.2 | 11.2 | 4.0 | 2.3 |
| 1996 | 8.8 | 12.3 | 4.2 | 2.6 |
| 1997 | 9.9 | 12.6 | 4.3 | 2.9 |
| 1998 | 9.2 | 13.5 | 4.3 | 2.8 |
| 1999 | 9.1 | 13.5 | 4.4 | 2.9 |
| 2000 | 9.4 | 14.3 | 4.5 | 3.5 |

Table 2.3 reveals the black carbon emission in other countries in South Asia are much less than the emissions from India. Fuel-wise BC emissions for South Asian countries are presented in Tables 2.4 to 2.7.

Table 2.4  Fuel wise BC emission (tonnes/year) from Bangladesh

|  | 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Hard coal | 1987.24 | 1146.98 | 1214.18 | 1073.94 | 1072.78 | 2457.2 | 1925.98 | 2705.46 | 1811.04 | 1637.8 | 1963.28 |
| LPG | 0.54 | 0.48 | 0.48 | 0.54 | 0.78 | 0.9 | 0.78 | 0.96 | 0.54 | 0.6 | 0.78 |
| Gas/diesel oil | 583.1 | 564.9 | 644 | 663.6 | 674.1 | 857.5 | 918.4 | 1037.4 | 1080.8 | 1037.4 | 931.7 |
| Kerosene | 142.5 | 116.4 | 107.7 | 112.5 | 117.6 | 130.2 | 135.6 | 161.7 | 175.8 | 175.8 | 158.4 |
| Gasoline | 9.8 | 10.7 | 12 | 13.8 | 15.3 | 18.7 | 20.9 | 27.9 | 27.2 | 27.2 | 26.9 |
| Biomass (Fuelwood) | 5120 | 5225 | 5337 | 5455 | 5577 | 5693 | 5812 | 5933 | 6057 | 6183 | 6312 |
| Total | 7843 | 7064 | 7315 | 7319 | 7458 | 9158 | 8814 | 9867 | 9152 | 9062 | 9393 |

Table 2.5  Fuel wise BC emission (tonnes/year) from Pakistan

|  | 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Coal | 3143 | 3055 | 3099 | 3267 | 3713 | 3238 | 3837 | 3756 | 3366 | 3673 | 3174.8 |
| LPG | 7.62 | 8.82 | 7.86 | 8.1 | 7.32 | 10.26 | 12.3 | 11.22 | 12.36 | 14.1 | 19.14 |
| Gasoline | 82.1 | 82.9 | 89.9 | 98.9 | 99.2 | 98.3 | 106.2 | 119.7 | 122.3 | 117.1 | 107.6 |
| Kerosene | 339.9 | 288.6 | 189.6 | 192 | 182.4 | 180.6 | 184.2 | 156.6 | 154.2 | 150 | 133.5 |
| Diesel | 1283.1 | 1291.5 | 1510.8 | 1650.3 | 1773.6 | 1844.7 | 1980 | 1921.5 | 1952.7 | 2055.3 | 2180.7 |
| FO | 2171 | 2290 | 2708 | 2981 | 3570 | 3938 | 4692 | 4871 | 5464 | 5165 | 5732 |
| Biomass (Fuelwood) | 4401 | 4526 | 4665 | 4840 | 4995 | 5176 | 5363 | 5558 | 5759 | 5968 | 6184 |
| Total | 8284.4 | 8487.5 | 9170.8 | 9770.6 | 10627.5 | 11247.7 | 12338.1 | 12638.0 | 13464.9 | 13469.7 | 14357.4 |

Table 2.6  Fuel wise BC emission (tonnes/year) from Nepal

|  | 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Hard Coal | 82 | 92 | 111 | 104 | 115 | 123 | 274 | 297 | 323 | 351 | 351 |
| LPG | 0.24 | 0.36 | 0.48 | 0.6 | 0.78 | 1.08 | 1.32 | 1.74 | 2.34 | 2.34 | 2.4 |
| Gasoline | 1.6 | 2.7 | 2.6 | 2.2 | 2.5 | 3.2 | 3.2 | 3.5 | 3.7 | 4 | 4.2 |
| Kerosene | 23.1 | 37.5 | 35.4 | 38.4 | 39 | 52.2 | 58.5 | 66.9 | 69.3 | 78.3 | 73.8 |
| Diesel oil | 77 | 118.3 | 113.4 | 116.9 | 127.4 | 157.5 | 153.3 | 178.5 | 189.7 | 184.1 | 189 |
| Fuel oil | 4.2 | 4.2 | 9.1 | 11.2 | 10.5 | 4.9 | 4.9 | 8.4 | 9.8 | 9.1 | 13.3 |
| Biomass (Fuelwood) | 3234 | 3319 | 3406 | 3496 | 3587 | 3620 | 3660 | 3700 | 3741 | 3782 | 3823 |
| Total | 3422 | 3574 | 3678 | 3769 | 3882 | 3962 | 4155 | 4256 | 4339 | 4411 | 4457 |

Table 2.7  Fuel wise BC emission (tonnes/year) from Sri Lanka

|  | 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Coal | 9 | 2 | 1 | 2 | 1 | 5 | 1 | 1 | 1 | 1 | 1 |
| LPG | 2.04 | 2.28 | 2.64 | 3.12 | 3.84 | 4.32 | 5.22 | 5.94 | 6.78 | 7.98 | 9 |
| motor gasoline | 17.9 | 15.9 | 16.5 | 17.3 | 18.4 | 18.8 | 19.8 | 19.5 | 20.4 | 21.3 | 22.4 |
| Other kerosene | 50.1 | 48.3 | 56.7 | 57.3 | 62.4 | 67.2 | 68.7 | 67.5 | 70.8 | 73.2 | 68.7 |
| Diesel oil | 384 | 413 | 550 | 521 | 563 | 615 | 839 | 1183 | 997 | 1141 | 1211 |
| Fuel oil | 87.5 | 102 | 176.4 | 176.4 | 162.4 | 108.5 | 253.4 | 329 | 445.9 | 449.4 | 514.5 |
| Biomass (Fuelwood) | 1521 | 1541 | 1560 | 1581 | 1604 | 1610 | 1630 | 1650 | 1670 | 1690 | 1711 |
| Total | 2071 | 2124 | 2363 | 2358 | 2415 | 2429 | 2817 | 3256 | 3212 | 3384 | 3538 |

For Bhutan, data on fuel wood consumption only was available and BC emissions were estimated for the same. The BC estimates are 0.23Gg in 1990; 0.23 Gg in 1991; 0.24 Gg in 1992; 0.24 Gg in 1993; 0.25 Gg  in 1994; 0.25 Gg in 1995; 0.25 Gg in 1996; 0.25 Gg  0.25 Gg in 1997; 0.26 Gg in 1998; 0.26 Gg in 1999 and  0.27 Gg in 2000.

# Text boxes

2