Sulphur dioxide emission inventory

3.1 Introduction

The energy consumption data as reported in Chapter 1 along with appropriate emission factors (based on literature survey) were used to estimate the emission inventory for sulphur dioxide in India. The emission factors used in the current study along with those used in some of the earlier studies are given in Table 3.1.

Table 3.1  Sulphur dioxide emission  factors

| Source category (Energy consumption) | Emission Coefficient (Tonne/Tonne) |
| --- | --- |
|  | Current study | Garg et. al. 2002 | Reddy et. al., 2002 (a,b)* |
| Coal | Variable Indian emission factor (e.g., 0.008466 & 0.0664 for coal consumption in power sector and 0.016875 & 0.04725 for lignite) | 0.0102 | Variable emission rates based on S content |
| High Speed Diesel | 0.02 and 0.01 | 0.02 | 0.02 and 0.01 |
| Motor Spirit | 0.004 | 0.01 | 0.004 |
| Kerosene | 0.005 | 0.005 | 0.004 |
| Light Diesel Oil | 0.04 | 0.04 | 0.036 |
| Fuel oil | 0.08 | 0.08 | 0.08 |
| Low Sulphur Heavy Stock | 0.04 | 0.04 | 0.04 |
| LPG | 0.0004 | -- | 0.0004 |
| Fuel wood | 0.00048 | 0.0008 | 0.00048 |
| Agricultural Crop Residue | 0.00048 | 0.0006 | 0.00048 |
| Dung Cakes | 0.00084 | 0.0006 | 0.00084 |

* calculated based on S content specified in the paper.

In the current study, the coal emissions from power plants are based on Indian emission factor (CPCB 1994) i.e., 16.6 S Kg/T of Coal and 13.5 S Kg/T of Lignite. Also, the sulphur content of coal in the North East (Assam) is higher than the average sulphur content of other coal fields in India. Accordingly, the sulphur content of coal produced in North Eastern states is taken as 4% while that in the rest of the country is taken as 0.51% (Garg et. al., 2002; CIL, 1993).  Likewise, the sulphur content of lignite produced in Tamil Nadu and Gujarat is taken as 1.25 % and 3.5 %, respectively (CIL, 1993). In the industrial sector, the rate of atmospheric release of sulphur is assumed at 77.5% as the combustion temperature are lower than in utilities and result in higher sulphur retention in ash (Kato 1996; Reddy et. al., 2002a). Accordingly, in the current study, the SO2 emission factors are taken as 0.00775 tonne/tonne (all states except NE) and 0.062 tonne/tonne (NE states), respectively.

In the case of diesel, there has been a reduction in sulphur content over the years and the same has been accounted for. The sulphur content in diesel has reduced from 1% in 95-96 to 0.5% from 96-97 onwards. Also, in Delhi and other metro cities, it has come down to 0.25% from 98-99 onwards.  The sulphur reduction in petrol (from 0.2% to 0.1%) has come down only from April 2000 onwards.

3.2 Sulphur dioxide emission estimates for India

Based on the energy consumption data and the SO2 emission factors as discussed above, the sulphur dioxide emission estimates were made for various states for different fuel consumed and the same are given in Table 3.2 and Figure 3.1. Detailed fuel-wise and sector-wise SO2 emission estimates for India for the period 1990-91 to 1999-00 are given in Annexures V and VI, respectively.

Table 3.2   Fuel-wise SO2 emissions for India (in Thousand Tonnes) during the period 1990-91 to 1999-00

| Fuel | 90-91 | 91-92 | 92-93 | 93-94 | 94-95 | 95-96 | 96-97 | 97-98 | 98-99 | 99-00 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Coal | 1609 | 1770 | 1876 | 2107 | 2026 | 2203 | 2325 | 2385 | 2292 | 2432 |
| Lignite | 309 | 374 | 381 | 431 | 446 | 524 | 538 | 539 | 543 | 402 |
| High Speed Diesel | 424 | 435 | 490 | 517 | 567 | 642 | 351 | 360 | 362 | 385 |
| Motor Spirit | 14 | 14 | 14 | 15 | 17 | 19 | 20 | 21 | 22 | 24 |
| Kerosene | 42 | 42 | 43 | 45 | 45 | 47 | 48 | 49 | 53 | 54 |
| Light Diesel Oil | 59 | 57 | 55 | 54 | 54 | 52 | 48 | 48 | 50 | 60 |
| Fuel oil | 350 | 389 | 414 | 394 | 462 | 501 | 494 | 511 | 496 | 529 |
| Low Sulphur Heavy Stock | 177 | 165 | 159 | 165 | 162 | 168 | 174 | 176 | 180 | 188 |
| LPG | 1 | 1 | 1 | 1 | 1 | 2 | 2 | 2 | 2 | 2 |
| Sub-total Fossil Fuel | 2986 | 3248 | 3434 | 3730 | 3780 | 4156 | 4000 | 4091 | 4000 | 4175 |
| Fuel wood | 70 | 72 | 73 | 74 | 75 | 76 | 77 | 78 | 79 | 80 |
| Agricultural Crop Residue | 42 | 42 | 42 | 42 | 42 | 42 | 43 | 43 | 43 | 43 |
| Dung Cakes | 90 | 89 | 89 | 89 | 88 | 88 | 88 | 87 | 87 | 87 |
| Biomass Open Burning | 30 | 32 | 34 | 34 | 36 | 35 | 39 | 37 | 38 | 40 |
| Sub-total Biomass | 233 | 236 | 238 | 239 | 242 | 241 | 246 | 245 | 247 | 250 |
| Total | 3219 | 3484 | 3671 | 3969 | 4022 | 4397 | 4246 | 4335 | 4247 | 4424 |

Note: Totals may not add due to rounding off

The sulphur dioxide emission estimates were also made for various states for different sectors (Transport, Industry, Power, Domestic, Miscellaneous, and Open biomass burning) and the same are given in Table 3.3 and Figure 3.2.

Table 3.3   Sectoral SO2 emissions for India (in Thousand Tonnes) during the period 1990-91 to 1999-00

| Sector | Power | Industry | Transport | Domestic | Miscellaneous | Biomass Open Burning | Total |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 1990-91 | 1504 | 984 | 306 | 246 | 149 | 30 | 3219 |
| 1991-92 | 1697 | 1042 | 308 | 246 | 158 | 32 | 3484 |
| 1992-93 | 1810 | 1065 | 342 | 248 | 173 | 34 | 3671 |
| 1993-94 | 1958 | 1169 | 365 | 251 | 191 | 34 | 3969 |
| 1994-95 | 2030 | 1072 | 393 | 252 | 238 | 36 | 4022 |
| 1995-96 | 2298 | 1111 | 446 | 254 | 253 | 35 | 4397 |
| 1996-97 | 2391 | 1140 | 259 | 257 | 160 | 39 | 4246 |
| 1997-98 | 2467 | 1130 | 254 | 259 | 189 | 37 | 4335 |
| 1998-99 | 2360 | 1131 | 257 | 264 | 197 | 38 | 4247 |
| 1999-00 | 2443 | 1184 | 271 | 266 | 222 | 40 | 4424 |

Note: The miscellaneous sector includes agriculture and Misc. services (including DGS&D - Directorate General of Supplies and  Disposal) for petroleum products

The total SO2 emissions vary from 3.2 million tonnes (MT) to 4.4 MT during the period 1990-91 to 1999-00. These are somewhat comparable to other recent estimates i.e., 4.64 MT in 1995 by Garg. et.al., 2002 (including 0.119 MT from non-energy sources) and  4.35 MT  (4.03 MT from fossil fuel and 0.32 MT from biomass combustion) in 1996-97 by Reddy et. al., 2002 (a,b).  The current estimates are however, slightly on the lower side compared to both the earlier studies. This is due to the use of Indian emission factors for coal based power plants as well as appropriate accounting for the changes in the diesel fuel quality over the years.

It should however be noted that the current estimates are lower than earlier estimates for India i.e., 5.61 MT in 1995 and 6.28 MT in 1997 by Streets et. al. (2000); 5.10 MT in 1987-88 by Arndt et. al, 1997; 4.472 MT in 1990 by Foell et. al., 1995.

3.3 Sulphur dioxide emission estimates for other South Asian countries

Besides India, SO2 emissions were estimated for other South Asian countries (Bangladesh, Pakistan, Nepal, SriLanka) for which energy consumption data was compiled as discussed in Chapter 1. Primarily, the fuels considered were Coal, Petroleum products and Fuelwood.

An attempt has been made to use country specific emission factors, wherever available. For some of the fuel types, information related to sulphur content of fuels/ emission factors was adopted from the country specific reports compiled as part of Malé Declaration on control and prevention of air pollution and its likely transboundary effects for South Asia which were available from the website http://www.rrcap.unep.org/issues/air/maledec accessed in June 2004. However, in the absence of country specific information, default emission factors for India were used.

The total SO2 emissions are maximum in Pakistan and vary from 634 – 981 thousand tonnes during the period 1990-2000 (refer Table 3.4). Likewise, the SO2 emissions for Bangladesh, Nepal and SriLanka vary from 39-45, 2-9, and 20-82 thousand tonnes, respectively during the period 1990-2000. These emissions are much less as compared to the emissions from India that are in the range 3219-4424 thousand tonnes during 1990-2000.

Table 3.4  Total SO2 emissions (in Thousand Tonnes) from other South Asian countries

| Year | Bangladesh | Pakistan | Nepal | Srilanka |
| --- | --- | --- | --- | --- |
| 1990 | 48 | 641 | 8 | 23 |
| 1991 | 40 | 632 | 8 | 25 |
| 1992 | 45 | 695 | 9 | 35 |
| 1993 | 51 | 735 | 9 | 34 |
| 1994 | 50 | 834 | 9 | 34 |
| 1995 | 63 | 833 | 10 | 29 |
| 1996 | 47 | 959 | 12 | 50 |
| 1997 | 56 | 940 | 13 | 67 |
| 1998 | 50 | 974 | 14 | 73 |
| 1999 | 56 | 976 | 15 | 76 |
| 2000 | 56 | 991 | 16 | 85 |

The detailed fuel-wise break-up of SO2 emissions in Bangladesh, Pakistan, Nepal and SriLanka are given in Table 3.5  for the period 1990-2000.

Table 3.5  Fuel-wise SO2 emissions (in Tonnes) for South Asian countries (Bangladesh, Pakistan, Nepal and SriLanka) during the period 1990-2000.

| Country/Fuel | 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Bangladesh |  |  |  |  |  |  |  |  |  |  |  |
| Coal | 4363 | 1395 | 1310 | 488 | 457 | 4976 | 2728 | 5007 | 1442 | 713 | 5115 |
| LPG | 4 | 3 | 3 | 4 | 5 | 6 | 5 | 6 | 4 | 4 | 5 |
| Motor Spirit | 98 | 107 | 120 | 138 | 153 | 187 | 209 | 279 | 272 | 272 | 269 |
| Kerosene | 2375 | 1940 | 1795 | 1875 | 1960 | 2170 | 2260 | 2695 | 2930 | 2930 | 2640 |
| Diesel | 16660 | 16140 | 18400 | 18960 | 19260 | 24500 | 13120 | 14820 | 15440 | 14820 | 13310 |
| Fuel Oil | 15760 | 11920 | 14160 | 19920 | 18560 | 20960 | 18480 | 23440 | 19520 | 26880 | 23440 |
| Sub-total Fossil Fuel | 39260 | 31505 | 35788 | 41385 | 40395 | 52799 | 36802 | 46247 | 39607 | 45619 | 44779 |
| Fuel wood | 8777 | 8958 | 9148 | 9351 | 9560 | 9760 | 9963 | 10171 | 10383 | 10600 | 10821 |
| Sub-total Biomass | 8777 | 8958 | 9148 | 9351 | 9560 | 9760 | 9963 | 10171 | 10383 | 10600 | 10821 |
| Total | 48037 | 40463 | 44936 | 50736 | 49956 | 62558 | 46766 | 56418 | 49991 | 56219 | 55600 |
| Pakistan |  |  |  |  |  |  |  |  |  |  |  |
| Coal | 351487 | 332178 | 344937 | 351405 | 392734 | 355043 | 406329 | 376259 | 356603 | 377100 | 335981 |
| LPG | 51 | 59 | 52 | 54 | 49 | 68 | 82 | 75 | 82 | 94 | 128 |
| Motor Spirit | 164 | 166 | 180 | 198 | 198 | 197 | 212 | 239 | 245 | 234 | 215 |
| Kerosene | 4532 | 3848 | 2528 | 2560 | 2432 | 2408 | 2456 | 2088 | 2056 | 2000 | 1780 |
| Diesel | 85540 | 86100 | 100720 | 110020 | 118240 | 122980 | 132000 | 128100 | 130180 | 137020 | 145380 |
| Fuel Oil | 192060 | 202260 | 238500 | 262440 | 312120 | 343740 | 408360 | 423540 | 475140 | 449160 | 497340 |
| Sub-total Fossil Fuel | 633834 | 624610 | 686917 | 726676 | 825773 | 824436 | 949439 | 930302 | 964306 | 965609 | 980824 |
| Fuel wood | 7545 | 7759 | 7997 | 8298 | 8562 | 8873 | 9194 | 9527 | 9873 | 10231 | 10601 |
| Sub-total Biomass | 7545 | 7759 | 7997 | 8298 | 8562 | 8873 | 9194 | 9527 | 9873 | 10231 | 10601 |
| Total | 641380 | 632369 | 694914 | 734974 | 834335 | 833309 | 958633 | 939829 | 974179 | 975839 | 991425 |

| Country/Fuel | 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Nepal |  |  |  |  |  |  |  |  |  |  |  |
| Coal | 1240 | 1391 | 1679 | 1577 | 1741 | 1854 | 4128 | 4471 | 4867 | 5287 | 6472 |
| LPG | 2 | 2 | 3 | 4 | 5 | 7 | 9 | 12 | 16 | 16 | 16 |
| Motor Spirit | 15 | 25 | 24 | 20 | 23 | 29 | 29 | 32 | 34 | 37 | 39 |
| Kerosene | 246 | 400 | 378 | 410 | 416 | 557 | 624 | 714 | 739 | 835 | 787 |
| Diesel | 550 | 845 | 810 | 835 | 910 | 1125 | 1095 | 1275 | 1355 | 1315 | 1350 |
| Fuel Oil | 36 | 66 | 120 | 150 | 156 | 78 | 78 | 156 | 174 | 156 | 114 |
| Sub-total Fossil Fuel | 2088 | 2729 | 3013 | 2996 | 3251 | 3650 | 5963 | 6659 | 7184 | 7645 | 8778 |
| Fuel wood | 5545 | 5690 | 5839 | 5994 | 6148 | 6309 | 6474 | 6643 | 6816 | 6994 | 7176 |
| Sub-total Biomass | 5545 | 5690 | 5839 | 5994 | 6148 | 6309 | 6474 | 6643 | 6816 | 6994 | 7176 |
| Total | 7633 | 8419 | 8852 | 8989 | 9399 | 9959 | 12437 | 13301 | 14000 | 14639 | 15954 |
| Srilanka |  |  |  |  |  |  |  |  |  |  |  |
| Coal | 124 | 16 | 16 | 16 | 16 | 78 | 16 | 16 | 16 | 16 | 16 |
| LPG | 14 | 15 | 18 | 21 | 26 | 29 | 35 | 54 | 62 | 67 | 60 |
| Motor Spirit | 36 | 32 | 33 | 35 | 37 | 38 | 40 | 39 | 41 | 43 | 45 |
| Kerosene | 67 | 64 | 76 | 76 | 83 | 90 | 92 | 90 | 94 | 98 | 92 |
| Diesel | 8768 | 9440 | 12576 | 11904 | 12864 | 14064 | 19168 | 27088 | 22864 | 26144 | 27680 |
| Fuel Oil | 11130 | 12460 | 19320 | 19460 | 18690 | 12320 | 27650 | 36540 | 46970 | 46970 | 53690 |
| Sub-total Fossil Fuel | 20138 | 22027 | 32038 | 31511 | 31715 | 26618 | 47000 | 63826 | 70047 | 73337 | 81582 |
| Fuel wood | 2608 | 2641 | 2674 | 2710 | 2750 | 2791 | 2832 | 2873 | 2916 | 2959 | 3002 |
| Sub-total Biomass | 2608 | 2641 | 2674 | 2710 | 2750 | 2791 | 2832 | 2873 | 2916 | 2959 | 3002 |
| Total | 22746 | 24668 | 34712 | 34221 | 34466 | 29408 | 49831 | 66700 | 72963 | 76295 | 84584 |

For Bhutan, data on fuelwood consumption only was available and the SO2 emissions were estimated for the same. The SO2 emissions due to fuelwood burning during the years 1990 to 2000 are 399, 404, 408, 412, 417, 423, 429, 436, 442,449,455 tonnes, respectively.

3.4 Way forward

It is important to have an updated energy consumption data as well as regional emission factors. Both of them would contribute to realistic emission estimates for the countries in the region. Actual measurement of emission factors for Indian/other South Asian sources including efficiency of pollution control equipment, retention of sulphur in ash, on-road vehicular emission characteristics, better estimates from domestic sources, etc are needed for further refinement of these estimates. Thus, separate studies/projects are possibly required to address these issues.

Figure 3.1  Fuelwise emissions of SO2 from India for the years 1990-91 and 1999-00

# Text boxes

3

Table 3.5  contd……./-

Figure 3.2   Sectoral emissions of SO2 from India during the period 1990-91 to 1999-00