chapter 3  Sulphur dioxide emission inventory

Introduction

Anthropogenic atmospheric aerosols are known to be significant climate forcing agents. The climate effect of aerosols is quite complex. Some aerosols such as black carbon are believed to cause warming while others such as sulphates cause cooling.  Better quantification of emissions inventory for the aerosols is essential for model simulations.

This chapter focuses on the comprehensive estimation of sulphur dioxide emissions from both fossil fuel and biomass combustion from different states in India during the period 1950-2020.  In addition, estimation of sulphur dioxide emissions at the national level from other South Asian countries is also carried out.

Methodology

The energy consumption data as reported in Chapter 1 along with appropriate emission factors, based on literature survey, were used to estimate the emission inventory for sulphur dioxide in India. The emission factors used in the current study along with those used in some of the earlier studies are given in Table 3.1.

Table 3.1  Sulphur dioxide emission  factors

| Source category (Energy consumption) | Emission Coefficient (Tonne/Tonne) |
| --- | --- |
|  | Current study | Garg et. al. 2002 | Reddy et. al., 2002 (a,b)* |
| Coal | Variable Indian emission factor (e.g., 0.008466 & 0.0664 for coal consumption in power sector and 0.016875 & 0.04725 for lignite) | 0.0102 | Variable emission rates based on S content |
| High Speed Diesel | 0.02, 0.01,0.005,0.001, 0.0007,0.0001 | 0.02 | 0.02 and 0.01 |
| Motor Spirit | 0.004, 0.002,0.001, 0.0003,0.0001 | 0.01 | 0.004 |
| Kerosene | 0.005 | 0.005 | 0.004 |
| Light Diesel Oil | 0.04 | 0.04 | 0.036 |
| Fuel oil | 0.08 | 0.08 | 0.08 |
| Low Sulphur Heavy Stock | 0.04 | 0.04 | 0.04 |
| LPG | 0.0004 | -- | 0.0004 |
| Fuel wood | 0.00048 | 0.0008 | 0.00048 |
| Agricultural Crop Residue | 0.00048 | 0.0006 | 0.00048 |
| Dung Cakes | 0.00084 | 0.0006 | 0.00084 |

* calculated based on S content specified in the paper.

In the current study, the coal emissions from power plants are based on Indian emission factor (CPCB 1994) i.e., 16.6 S Kg/T of Coal and 13.5 S Kg/T of Lignite. Also, the sulphur content of coal in the North East (Assam) is higher than the average sulphur content of other coal fields in India. Accordingly, the sulphur content of coal produced in North Eastern states is taken as 4% while that in the rest of the country is taken as 0.51% (Garg et. al., 2002; CIL, 1993).  Likewise, the sulphur content of lignite produced in Tamil Nadu and Gujarat is taken as 1.25 % and 3.5 %, respectively (CIL, 1993). In the industrial sector, the rate of atmospheric release of sulphur is assumed at 77.5% as the combustion temperature are lower than in utilities and result in higher sulphur retention in ash (Kato 1996; Reddy et. al., 2002a). Accordingly, in the current study, the SO2 emission factors are taken as 0.00775 tonne/tonne (all states except NE) and 0.062 tonne/tonne (NE states), respectively.

In the case of diesel, there has been a reduction in sulphur content over the years and the same has been accounted for. The sulphur content in diesel has reduced from 1% pre-1996 to 0.5% after April 1996. Further, the sulphur content came down to 0.25 % and 0.05% in the entire country from January, 2000 and April, 2005, respectively. In Delhi and other major cities, the dates for implementation were advanced. The future improvements in fuel quality have been accounted for as per the auto-fuel policy of the government (Mashelkar R. A. , et al., 2002). In Delhi and other major cities, sulphur content has come down to 350 mg/Kg from April 2005 and the same would come into effect in the entire country from 2010. The sulphur content would be further reduced to 50 mg/Kg in the major cities in 2010.

Likewise, the sulphur content in petrol has reduced from 0.2% (pre-2000) to 0.1%  from April 2000 onwards in the entire country. It has been further reduced to 0.05% from April 2005 onwards in the entire country. In Delhi and other major cities, the sulphur content has come down to 150 mg/Kg from April 2005. As per the auto-fuel policy, in 2010, the sulphur content in petrol in the entire country would be reduced to 150 mg/Kg, and in the major cities, it would be further reduced to 50 mg/Kg.

Sulphur dioxide emission estimates for India

Based on the energy consumption data and the SO2 emission factors as discussed above, the sulphur dioxide emission estimates were made for various states for different fuel consumed and the same are given in Table 3.2 and Figure 3.1. Detailed fuel-wise and sector-wise SO2 emission estimates for India for the period 1950-2020 are given in Annexures V and VI, respectively.

Table 3.2   Fuel-wise SO2 emissions for India (in Thousand Tonnes) during the period 1950-2020

| Year | Coal | FO | LDO | HSD | MS | Lignite | HSS | Kerosene | LPG | Sub-total fossil fuel | Biofuel | Total SO2 emission (‘000 T) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1950 | 269 | 59 | 8 | 14 | 1 | 0 | 7 | 3 | 0 | 361 | 93 | 454 |
| 1955 | 275 | 86 | 12 | 20 | 2 | 0 | 10 | 5 | 0 | 409 | 93 | 502 |
| 1960 | 398 | 139 | 20 | 33 | 3 | 0 | 16 | 8 | 0 | 615 | 108 | 724 |
| 1965 | 543 | 207 | 30 | 49 | 4 | 0 | 23 | 11 | 0 | 867 | 119 | 986 |
| 1970 | 579 | 334 | 48 | 78 | 7 | 0 | 37 | 18 | 0 | 1102 | 128 | 1230 |
| 1975 | 773 | 333 | 34 | 132 | 5 | 0 | 61 | 15 | 0 | 1353 | 145 | 1497 |
| 1980 | 920 | 364 | 46 | 207 | 6 | 127 | 100 | 21 | 0 | 1791 | 206 | 1997 |
| 1985 | 1275 | 619 | 44 | 296 | 9 | 179 | 159 | 31 | 0 | 2613 | 223 | 2836 |
| 1990 | 1609 | 350 | 60 | 424 | 14 | 309 | 177 | 42 | 1 | 2987 | 202 | 3189 |
| 1995 | 2203 | 501 | 52 | 642 | 19 | 524 | 168 | 47 | 2 | 4156 | 206 | 4362 |
| 2000 | 2634 | 507 | 55 | 183 | 13 | 522 | 200 | 53 | 3 | 4169 | 210 | 4379 |
| 2005 | 3350 | 558 | 58 | 50 | 9 | 740 | 262 | 66 | 5 | 5097 | 210 | 5307 |
| 2010 | 4065 | 612 | 62 | 43 | 3 | 959 | 324 | 78 | 7 | 6153 | 210 | 6363 |
| 2015 | 4780 | 666 | 66 | 52 | 4 | 1177 | 386 | 91 | 9 | 7231 | 209 | 7441 |
| 2020 | 5496 | 720 | 70 | 61 | 5 | 1395 | 448 | 104 | 11 | 8309 | 209 | 8519 |

The total SO2 emissions vary from 0.45 million tonnes (MT) to 8.59 MT during the period 1950-2020. Table 3.2 indicates the decreasing share of bio-fuels to the total SO2 emissions over the years due to the increasing usage of the fossil fuels in the overall energy consumption pattern. Thus, while fossil fuels and bio-fuels contributed to 80% and 20%, respectively to the total SO2 emissions in 1950, this ratio changed to 95% and 5%, respectively in 2000. Also, in terms of share of SO2 emissions, coal continues to be the dominant source throughout the study period.  In the year 2000, the share of coal, lignite and fuel oil were 60%, 12%, and 12%, respectively to the total SO2 emissions. However, the share of high speed diesel to the total SO2 emissions has declined from 15% in 1995 to 4% in 2000.

Figure 3.1  Trend of SO2 emissions from India for the period 1950-2020

Figure 3.1 clearly shows that fossil fuels are the dominant contributor to SO2 emissions. Also, significant fuel quality improvements in terms of reduction of sulphur content in diesel and petrol has had positive impact in terms of flattening the curve during the period 1995-2000.

The sulphur dioxide emission estimates were also made for various states for different sectors (Transport, Industry, Power, Domestic, Agriculture, and Miscellaneous and the same are given in Table 3.3 and Figure 3.2.

Table 3.3   Sectoral SO2 emissions for India (in Thousand Tonnes) during the period 1950-2020

| Year | Power | Industry | Transport | Agriculture | Domestic | Miscellaneous | Total |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 1950 | 190 | 127 | 25 | 6 | 96 | 10 | 454 |
| 1955 | 201 | 144 | 37 | 8 | 98 | 15 | 502 |
| 1960 | 295 | 216 | 59 | 13 | 116 | 24 | 724 |
| 1965 | 407 | 305 | 89 | 19 | 130 | 36 | 986 |
| 1970 | 464 | 388 | 143 | 31 | 146 | 58 | 1230 |
| 1975 | 607 | 486 | 153 | 41 | 160 | 51 | 1497 |
| 1980 | 880 | 571 | 207 | 56 | 227 | 56 | 1997 |
| 1985 | 1225 | 868 | 314 | 84 | 254 | 91 | 2836 |
| 1990 | 1508 | 980 | 306 | 89 | 245 | 61 | 3189 |
| 1995 | 2301 | 1108 | 446 | 138 | 254 | 115 | 4362 |
| 2000 | 2664 | 1146 | 142 | 57 | 265 | 104 | 4379 |
| 2005 | 3447 | 1377 | 65 | 35 | 279 | 105 | 5307 |
| 2010 | 4238 | 1621 | 58 | 36 | 294 | 116 | 6363 |
| 2015 | 5030 | 1867 | 66 | 40 | 308 | 129 | 7441 |
| 2020 | 5823 | 2113 | 75 | 44 | 322 | 142 | 8519 |

Note: The miscellaneous sector includes Misc. services (including DGS&D - Directorate General of Supplies and  Disposal) for petroleum products1

Figure 3.2   Sectoral emissions of SO2 from India during the period 1950-2020

Figure 3.2 shows that power and industry sector are the major contributors to SO2 emissions. In the year 2000, the share of power and industry were 61% and 26%, respectively, while domestic, transport and agriculture contributed to 6%, 3%, and 1%, respectively.

Sulphur dioxide emissions from open biomass burning

Estimates are made of the SO2 emissions due to open burning of agricultural crop residue and the same are presented in Table 3.4. These estimates are not projected for future years as the state-wise crop-wise agricultural production data was not available.

Table 3.4   Sulphur dioxide emissions from open biomass burning

| Year | Sulphur dioxide emissions ('000 Tonnes) |
| --- | --- |
| 1950 | 8.2 |
| 1955 | 10.7 |
| 1960 | 13.4 |
| 1965 | 12.3 |
| 1970 | 17.6 |
| 1975 | 19.4 |
| 1980 | 21.3 |
| 1985 | 25.2 |
| 1990 | 30.5 |
| 1995 | 34.7 |
| 2000 | 39.7 |

Monthly variation in sulphur dioxide emissions

Monthly variation in the sulphur dioxide emissions are estimated based on the variations observed in the monthly fuel consumption data for a period of two years, i.e., 1992-93 and 1993-94. The monthly variation in the consumption of various petroleum products was noted. However, the variation in the consumption of coal and lignite was considered only for the power sector, which incidentally happens to be the biggest consumer. Variation in the open crop residue burning was based on the crop harvesting data.

Figures 3.3 and 3.4 show the monthly variations in SO2 emission estimates from fossil fuel combustion and open biomass burning, respectively for 1992-93 and 1993-94. It is seen that the monthly variation in SO2 emission estimate from fossil fuel combustion is minimal, whereas in case of emissions from open burning of cross residue, the variation is significant. The variation in the emissions from crop burning follows the crop-harvesting season. Two-peak period (March- May and October-December) have been observed in the emissions. This is in accordance with the harvesting season of Rabi and Kharif crops.  Also, the dip in the monsoon period is clearly evident. However, since the share of open burning in the total emissions is comparatively less, thus these variations are greatly reduced while considering the variations in the monthly total emissions of SO2.

Figure 3.3   Monthly variation of SO2 emissions from fossil fuel combustion during the years    
                    1992-93 and 1993-94

Figure 3.4   Monthly variation of SO2 emissions from open biomass burning during the years 
                     1992-93 and 1993-94


Comparison of sulphur dioxide emission estimates from India

The total SO2 emissions in 1995 and 2000 are estimated to be 4.36 MT and 4.38 MT, respectively. These are somewhat comparable to other recent estimates i.e., 4.64 MT in 1995 by Garg. et.al., 2002 and  4.35 MT  (4.03 MT from fossil fuel) in 1996-97 by Reddy et. al., 2002 (a,b,c).  The current estimates are however, slightly on the lower side compared to Garg. et. al., 2002. This is due to the use of Indian emission factors for coal based power plants as well as appropriate accounting for the changes in the diesel / petrol fuel quality over the recent years.

It should however be noted that the current estimates are lower than other estimates for India i.e., 5.61 MT in 1995 and 6.28 MT in 1997 by Streets et. al. (2000); 5.54 MT in 2000 by Streets et. al. (2003); 5.10 MT in 1987-88 by Arndt et. al, 1997; 4.472 MT in 1990 by Foell et. al., 1995. This is due to use of recent energy consumption statistics as well as use of Indian emissions factors accounting for the changes in fuel quality.

Sulphur dioxide emission estimates for other South Asian countries

Besides India, SO2 emissions were estimated for other South Asian countries (Bangladesh, Pakistan, Nepal, Sri Lanka) for which energy consumption data was compiled as discussed in Chapter 1. Primarily, the fuels considered were coal, petroleum products and fuelwood.

An attempt has been made to use country specific emission factors, wherever available. For some of the fuel types, information related to sulphur content of fuels/ emission factors was adopted from the country specific reports compiled as part of Malé Declaration on control and prevention of air pollution and its likely trans-boundary effects for South Asia which were available from the website http://www.rrcap.unep.org/issues/air/maledec accessed in June 2004. However, in the absence of country specific information, default emission factors for India were used.

Amongst these countries, the total SO2 emissions are maximum in Pakistan followed by Sri Lanka, Bangladesh and Nepal. In the case of Pakistan, the SO2 emissions vary from 178 – 1925 thousand tonnes during the period 1950-2020 (Table 3.5). Likewise, the SO2 emissions for Sri Lanka, Bangladesh, Nepal vary from 53-137 , 28-134, and 2-39 thousand tonnes, respectively during the period 1950-2020 (1971 onwards in case of Bangladesh). These emissions are much less as compared to the emissions from India that are in the range 454-8519 thousand tonnes during the period 1950-2020.

The detailed fuel-wise break up of SO2 emissions in South Asian countries (Bangladesh, Pakistan, Nepal, and SriLanka) are given in Annexure VII.

Table 3.5  Total SO2 emissions (in Thousand Tonnes) from South Asian countries

| Year | Bangladesh | Sri Lanka | Pakistan | Nepal |
| --- | --- | --- | --- | --- |
| 1951 | - | 53 | 178 | 2 |
| 1956 | - | 43 | 214 | 2 |
| 1961 | - | 26 | 236 | 3 |
| 1966 | - | 28 | 269 | 3 |
| 1971 | 28 | 18 | 190 | 4 |
| 1976 | 46 | 20 | 165 | 4 |
| 1981 | 56 | 29 | 248 | 6 |
| 1986 | 55 | 20 | 440 | 7 |
| 1991 | 40 | 25 | 618 | 8 |
| 1996 | 47 | 45 | 925 | 13 |
| 2001 | 64 | 80 | 963 | 17 |
| 2005 | 70 | 86 | 1200 | 21 |
| 2010 | 91 | 103 | 1441 | 27 |
| 2015 | 113 | 120 | 1683 | 33 |
| 2020 | 134 | 137 | 1925 | 39 |